TVM instruction set

Terminology
A command is a specific action performed by a TVM expressed as a number.
A flag is a special number applied to a command to specify the command.
A statement is a collection of command, flag, and data.
Directives are special instructions that have a high priority and can affect the execution of a program or other commands.

nil is a low priority Directive indicating the absence of something (flag, data), code (0).

A list of commands, flags, and directives, and their General meaning.

Commands:
CRG – code (1) register selection
CRC – code (2) cell selection
PRG – code (3) put data in the zero cell of the selected register
PRC – code (4) put the data in the selected cell in the selected register
GJP – code (5) go to JPT with the selected code
COM – code (9) using the instruction with the selected code
PUT – code (10) display values
ACCADD – code (14) increases the value in the battery by the selected number of units.
ACCSUBT – code (15) reduces the value in the battery by the selected number of units.
CMP – code (16) comparison of register values.
INPUT – code (18) enter values using the keyboard.
ACCMULT – code (19) multiplication of the accumulator.
ACCDIV – code (20) accumulator division.

Flags:
The STDI – code (1) indicates that the data is a number
The STDA – code (2) indicates that the data is a register address
The STDC – code (3) indicates that the data is the address of the register in which the ASCII code of the character is located.
The CWR – code (4) indicates that the data is an ASCII character code.
The VWR – code (5) indicates that the data is a number.
ALL – code (6) indicates that the command applies to the entire code.
The ACC – code (7) indicates that the command is applied to the accumulator.

Directives:
JPT – code (6) creates a label.
The DEB – code (7) displays the number of the memory cell to be read.
MAIN – code (8) indicates the beginning of the program.
RESTART – code (11) starts execution of the program again.
The QUIT – code (12) terminates the program.
CLEAR – code (13) erase the program code from the memory.
The GOBACK – code (17) returns the program execution to the initial point.
END – code (3070) end of the program.

Instructions and their meaning:

Species conventions: I will use the following notation to refer to instructions:

[Command] [Flag / nil] [Data / nil]

[CRG] [STDI] [N] – select zero cell of register N.
[CRG] [STDA] [N] – select a specific register cell, N has the following form: RC, where R is the register number R >= 1, C is the register cell number C >= 0.

[CRC] [STDI] [N] – select cell N, the register previously selected using [CRG] [STDI] [N].

[PRG] [STDI] [N] – put the value of N in the zero cell of the register selected using [CRG] [STDI] [N].
[PRG] [STDA] [N] — put data In n in the selected register cell using [CRG] [STDA] [N].

[PRC] [STDI] [N] — select cell n of the selected register using [CRG] [STDI] [N].
[PRC] [STDA] [N, M] – moving values from register N to M, N and M have the following form: RC, where R is register number R >= 1, C is register cell number C >= 0.

[GJP] [N] [COND] – move to label N if COND > nil, labels can only be numbers.
[JPT] [N] [nil] - define label with number N.

[PUT] [STDI] [N] – is the output value of the register N as the number on the screen, N has the following form: RC, where R is the register number R >= 1, C is the number of the cells of register C >= 0.
[PUT] [STDC] [N] – is the output value of the register N as the symbol on the screen N has the following form: RC, where R is the register number R >= 1, C is the number of the cells of register C >= 0.
[PUT] [CWR] [N] — displays N as a character without registers.
[PUT] [VWR] [N] — output N as a number on the screen without registers.
[PUT] [ACC] [nil] – displays the register value as a number.

[DEB] [nil] [nil] — output of the currently read memory cell.
[MAIN] [nil] [nil] — start of the program.
[RESTART] [nil] [nil] — start the program again.
[QUIT] [nil] [nil] — immediate termination of the program.

[CLEAR] [ALL] [nil] – erases all program code before calling CLEAR.
[CLEAR] [N] [nil] – erases a specific memory location.

[ACCADD] [STDI] [nil] – increase the battery value by 1.
[ACCADD] [STDA] [N] — an addition to the value of the accumulator register value N, N has the following form: RC, where R is the register number R >= 1, C is the number of the cells of register C >= 0.
[ACCADD] [VWR] [N] - add the number N to the value in the accumulator.

[ACCSUBT] [STDI] [nil] – decrease the accumulator value by 1.
[ACCSUBT] [STDA] [N] — subtracting from the value of the accumulator register value N, N has the following form: RC, where R is the register number R >= 1, C is the number of the cells of register C >= 0.
[ACCSUBST] [VWR] [N] - subtraction of the number N from the accumulator value.

[CMP] [STDI] [N, M, K] — a comparison of N and M and outputs the result in the register K, K has the following form: RC, where R is the register number R >= 1, C is the number of the cells of register C >= 0. It should be taken into account that if K < 0, then N < M, if K > 0, then N > M, if K = 0, then N = M.

[GOBACK] [nil] [nil] – is used if the jump to a label need to come back.

[INPUT] [STDI] [N] – entering numeric values in the register N. N has the following form: RC, where R is the register number R >= 1, C is the register cell number C >= 0.
[INPUT] [STDA] [N] – enter character values in the register N. N has the following form: RC, where R is the register number R >= 1, C is the register cell number C >= 0.
[INPUT] [ACC] [nil] - enter numeric values into the battery.
[INPUT] [CACC] [nil] - enter character values into the battery.

[ACCMULT] [STDA] [N] — multiply the value of the accumulator to the value of the register N, N has the following form: RC, where R is the register number R >= 1, C is the number of the cells of register C >= 0.
[[ACCMULT] [VWR] [N] — multiply the value of the accumulator by the number N.

[ACCDIV] [STDA] [N] — divide the value of the accumulator to the value of the register N, N has the following form: RC, where R is the register number R >= 1, C is the number of the cells of register C >= 0.
[ACCDIV] [VWR] [N] - division of register value by N.